## Slide 1: Smart car parking
Nallagatla Manikanta COG16/04367 Palakonda Shiva Prasad COG16/07331
Keetha Indraneel Varma COG16/04357

## Slide 2: Problem statement
Conventionally, car parking systems do not have any intelligent monitoring. Parking lots are monitored by human beings. All vehicles enter into the parking and waste time searching for parking slots. Sometimes this can create blockages. Conditions worsen when there are multiple parking lanes and each lane has multiple parking slots. Use of automated system for car parking monitoring will reduce human efforts. 1. The system has to increment whenever a car is coming into the parking lot.
2. When a car leaves, the system has to decrement by 1 from the total count.
3. Assume parking lot is finite (restricted the limit of parking spots to be 1024)

## Slide 3: Multicar parking system

## Slide 4: Traditional car parking system

## Slide 5: introduction
Increase in population implies Number of Automoblies increase
Need of Automatic Car parking system
  Reduce Strain

## Slide 6: Our approach
Store the count of the number of cars in a variable
Whenever a new car comes:
  If count of cars less than the maximum limit:
    Allow car into parking area and increase the count
  Else close the gate
Whenever a car leaves from the parking area
  Decrease the count by one

## Slide 7: State table
A | B | Count | Count New
1 | 1 | <1024 | Count
1 | 0 | <1024 | Count+1
0 | 1 | <1024 | Count-1
0 | 0 | <1024 | Count
1 | 1 | =1024 | Count
1 | 0 | =1024 | Count
0 | 1 | =1024 | Count-1
0 | 0 | =1024 | Count

## Slide 8: State diagram
Past state
Present State
Next State
A = 0
B = 1
A = 1
B = 0
A = 0
B = 0
A = 1
B = 1

## Slide 9: Results Code
library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.STD_LOGIC_ARITH.ALL;
use IEEE.STD_LOGIC_UNSIGNED.ALL;
use ieee.numeric_std.all;

## Slide 10: Results
entity carParking is
port(
A : in std_logic;
B : in std_logic;
reset : in std_logic;
clock : in std_logic;
entranceA : out std_logic;
exitB : out std_logic;
count : out std_logic_vector(9 downto 0));
end carParking;

## Slide 11: Results
architecture Behavioral of carParking is
signal cou : std_logic_vector(9 downto 0);
begin
process(clock)
begin
if(rising_edge(clock)) then
if(reset = '1') then

## Slide 12: Results
cou(0) <= '0';
cou(1) <= '0';
cou(2) <= '0';
cou(3) <= '0';
cou(4) <= '0';
cou(5) <= '0';
cou(6) <= '0';
cou(7) <= '0';

## Slide 13: Results
cou(8) <= '0';
cou(9) <= '0';
entranceA <= '0';
exitB <= '0';
end if;
if(A = '1' and B = '0' and cou < "1111111111" and reset = '0') then
cou <= cou+1;
entranceA <= '1';
exitB <= '0';

## Slide 14: Results
if(A = '0' and B = '1' and cou > "000000000" and reset = '0') then
cou <= cou-1;
entranceA <= '0';
exitB <= '1';
end if;
end if;
end process

## Slide 15: Waveforms

## Slide 16: Waveforms

## Slide 17: Waveforms

## Slide 18: RTL SChematic
Notes: This schematic is generated after the HDL synthesis phase of the synthesis process. It shows a representation of the pre-optimized design in terms of generic symbols, such as adders, multipliers, counters, AND gates, and OR gates, that are independent of the targeted Xilinx device

## Slide 19: Advantages of smart car parking system
• Accurately predict and sense spot/vehicle occupancy in real-time.
• Guides residents and visitors to available parking.
• Optimize Parking Space Usage
• Help traffic in the city flow more freely leveraging IoT technology.
• Smart Parking plays a major role in creating better urban
environment by reducing the emission of CO2 and other pollutants

## Slide 20: CONclusion
Algorithm is implemented using VHDL language
using Xilinx 14.2 ISE interface

## Slide 21: REFERENCES
Automated parking system by Lina Lo in 2012
Smart Parking System with Image Processing Facility by M.O. Reza, M.F. Ismail, A.A. Rokoni, M.A.R. Sarkar in 2012.
Smart Parking Applications Using RFID Technology by Zeydin PALA and Nihat INAN in 2009 IEEE explore
Smart Parking by Gongjun Yan Weiming

## Slide 22: THANK YOU